## Slide 1: Single cycle RISC processor For Prof. Dr. Gihan Naguib Associate Professor, Department of Electrical Engineering. Eng. Jihad Awad Teaching Assistant, Department of Electrical Engineering
Fayoum University Faculty of Engineering Electronics & Electrical
Communications Department

## Slide 2: Program Counter
How It Works: The PC starts with an initial address (e.g., 0x0000). On each clock cycle (CLK), it either increments by 1 (PC+1) for sequential execution or updates to a new address for jumps/branches using Imm16 or JALR.

## Slide 3: Instruction Memory
Role: Stores program instructions to be executed by the CPU.
How It Works:The Instruction Memory fetches a 32-bit instruction from the address provided by the PC on each clock cycle and sends it for decoding.

## Slide 4: Register File
Diagram Overview: This FPGA design, created in a tool like Quartus, illustrates a register file (RF) implementation for a processor.
Register File (RF): Central block with 32 registers (R0-R31), each 32 bits wide, for data storage.
Registers are organized in a grid, connected via buses for reading/writing.
Control signals manage data flow and register selection.

## Slide 5: ALU
The ALU in this FPGA design Contains four blocks 1- Arithmetic block 2- Logical block 3- Shifter block 4- Comprator block

## Slide 6: Arithmetic Unit
The Arithmetic unit performs four operations 1- Addition 2- Subtraction 3- Multiplication for signed number 4- Multiplication for unsigned number
It sends a signal to indicate an overflow condition.

## Slide 7: Logical Unit
The Logical unit performs four operations: 1- AND operation 2- OR operation 3- NOR operation 4- XOR operation

## Slide 8: Shifter Unit
The shifter unit performs four operations: 1- Shift Left Logical 2- Shift Right Logical 3- Shift Right Arithmetic 4- Rotate Right

## Slide 9: Comparator Unit
The Comparator unit performs operations: 1- Set less than 2- Set less than unsigned 3- Set equal
The Comparator unit generates signals: 1- Branch Equal and Not Equal 2- Branch Greater Equal 3- Branch smaller 4- Branch smaller unsigned 5- Branch Greater Equal unsigned

## Slide 10: Data Memory
Role: The DM block acting as the main memory, stores and retrieves data for a processor while working with the RF for efficient data management.

## Slide 11: Main Control Unit
Role: The Main Control Unit (MCU) decodes the OPcode to generate control signals for the processor’s operation.

## Slide 12: ALU Control Unit
Role: The ALU Control unit in this FPGA design generates specific operation signals for the Arithmetic Logic Unit (ALU) based on the OPCODE and Funct inputs.

## Slide 13: PC control Unit
Role: The PC Control unit manages program counter (PC) updates by determining branch conditions based on the OPCode

## Slide 14: Thank You! This project reflects our dedication and teamwork
Meet Our Team:
Raghad Soliman Mohamed
Yusuf Mohamed Saleh Boriek
Abdulrahman Abdulnasser Abdulrahman ✨Great achievements come from great teamwork✨